## Slide 1: Master-Thesis Presentation by Özcan Karaca Testbed-Development for lectureStudio
Testbed-Development for lectureStudio
Testbed-Entwicklung für lectureStudio
Fachgebiet Echtzeitsysteme
Fachbereich Elektrotechnik und
Informationstechnik
Technische Universität Darmstadt
25.03.2024

## Slide 2: Motivation
Motivation
Server
Client
25.03.2024
A P2P Algorithm for lectureStudio
  Direct Distribution Among Clients
  Reducing the Central Server's Load
  Optimizing Bandwidth
Developing A Container-Based Testbed Environment for the P2P Algorithm
  Simulation of Real Network Data
  Configuration and Validation of the Network Characteristics
  Communication and Data Transfer between Nodes
Client
Client
Client
Server
Client
Client
Relay-Client
Client
Performance Evaluation of the P2P Algorithm
  Analysis of Resource Consumption
  Analysis of Total Duration

## Slide 3: Task Description
TASK DESCRiption
25.03.2024
Finding Real Network Data
  Maximum Upload Speed, Maximum Download Speed, Latency, and Packet Loss
Simulating Real Network Data Using Normal Distribution
Generating Network Topology
Integrating the P2P Algorithm
Configuring the Components of the P2P Algorithm in the Testbed
  Creating a Containerlab File and Configuring Network Management, Nodes and Links
Implementing and Validating the Network Characteristics of the Connections
  Bandwidth, Latency, and Packet Loss
Managing Communication and Data Transfer
  Tracking and Validating the Data Transfer Process
Evaluating of the Testbed and the P2P Algorithm Performance

## Slide 4: Initial Steps (Not Repeated) of the Testbed
1
2
3
4
5
Simulating Real Network Data
Mesh Network Topology
Network Topology Generator
Data Flow between Steps
Integrating the P2P Algorithm
Optimized Network Topology
25.03.2024
Simulating Real Network Data Using Normal Distribution
Generating Mesh Network Topology
  Integrating the P2P Algorithm
  Implementing the Traditional Server-Client Based Approach
Calculating Optimized Network Topology with the P2P Algorithm
INITAL steps (not repeated) of the testbed

## Slide 5: Simulating Real Network Data
Analyzing Real Network Dataset
  Max Download Speed, Max Upload Speed
  Latency
  Packet Loss
Reading Real Network Data from CSV File
Generating Network Data Using Normal Distribution
  Having Mean and Standard Deviation from UK and Germany Based Data
Name of Configuration | Mean (μ) | Standard Deviation (σ)
First Configuration | From UK-Based Data | From UK-Based Data
Second Configuration | From Ger-Based Data | From UK-Based Data
25.03.2024
        Simulating real network data
[1], [2]

## Slide 6: Network Topology
        Network Topology
{
"filename": "test.pdf",
"filesize": 5000,
"peers": [
{
"name": "lectureStudioServer",
"maxDownload": 29150,
"maxUpload": 9209
},
{
"name": "1",
"maxDownload": 1080,
"maxUpload": 373
}
]
}
"connections": [
{
"sourceName": "lectureStudioServer",
"targetName": "1",
"bandwidth": 1080,
"latency": 57,
"loss": 0.0035
},
{
"sourceName": "1",
"targetName": "lectureStudioServer",
"bandwidth": 373,
"latency": 57.15,
"loss": 0.0035
}
]
}
Network Topology Generated by the Testbed
{
"superpeers": [
{
"name": "1"
}
],
"peer2peer": [
{
"sourceName": "lectureStudioServer",
"targetName": "1"
},
{
"sourceName": "1",
"targetName": "2"
}
]
}
Network Topology Optimized by the P2P Algorithm
25.03.2024
Generating Network Topology by the Testbed
  Listing Nodes with Network Characteristics
  Detailing Connections between the LectureStudio Server and All Peers
Optimizing Network Topology by the P2P Algorithm
  Identifying Super Peers
  Optimizing Connections between the Studio Server and Peers

## Slide 7: Container—Based Testbed Environment
Docker and Containerlab: Efficient, Isolated Simulation Environment
Creation and Management of User-Defined Network Topologies
Advantages of Using Containerlab for the Testbed
  Properties of Containerlab
      name, image, kind, env, binds, etc.
  Speed, Ease of Use, Repeatability
  Creation of Complex Network Topologies
        Management of Container-Testbed Environment
[3]
name: testbed
topology:
nodes:
peer1:
kind: linux
image: image-testbed
peer2:
kind: linux
image: image-testbed
links:
- endpoints: [peer1:eth1, peer2:eth1]
Configuration of Containerlab File (YAML)
25.03.2024

## Slide 8: Execution Steps (Repeated) of the Testbed
lectureStudio-server
super-peer
peer
tracker-peer
Verifying the Connection Characteristics
1
4
5
3
6
2
Data Flow between Steps
Data Flow to Testbed
Definition of the Containerlab
1
Communication and Data Transfer
Configurating the Connection Characteristics
Checking the PDF File
Tracking the Data Transfer
25.03.2024
        Execution Steps (Repeated) of the Testbed

## Slide 9: Configuring the Components of the P2P Algorithm
25.03.2024
        Configuring the Testbed Environment
name: testbed
mgmt:
network: fixedips
ipv4-subnet: 172.100.100.0/24
topology:
nodes: …
links:
- endpoints: [lectureStudioserver:eth1, 1:eth1] - endpoints: [lectureStudioserver:eth2, 2:eth1] - endpoints: [lectureStudioserver:eth3, 3:eth1] - endpoints: [lectureStudioserver:eth4, 4:eth1] - endpoints: [lectureStudioserver:eth5, 5:eth1] - endpoints: [lectureStudioserver:eth6, 6:eth1] - endpoints: [5:eth2, 7:eth1] - endpoints: [6:eth2, 8:eth1] - endpoints: [6:eth3, 9:eth1] - endpoints: [6:eth4, 10:eth1]
Configuration of Containerlab File (Network Management, Nodes and Links)
lectureStudio server
super peer
peer
tracker peer
Configuration of Nodes

## Slide 10: Configuring and Verifying the Network Characteristics
        NeTwork topology configuration & verifying
Testbed
netem
eth0
bandwidth
latency
packet loss
Network Interface
Network Emulator
25.03.2024
Configurating the Connection Characteristics Using Traffic Control Commands
  Bandwidth Limitation
  Latency Addition
  Packet Loss Simulation
Configuring these Characteristics with Scripts
  Properties of Containerlab (exec, binds or cmd)
Verifying the Connection Characteristics
  Using Tools like ping, iperf3

## Slide 11: Connection Strategy Among Peers
        Connection and data distribution among peers
25.03.2024
lectureStudio server
Port:9090
IP:172.20.23.2
IP:172.20.24.2
IP:172.20.22.3
eth1
Port:7070
IP:172.20.21.2
IP:172.20.22.2
eth2
eth1
eth1
eth2
eth3
IP:172.20.24.3
IP:172.20.23.3
eth1
eth1
super peer
peer
peer
peer
Communication via IP Address and Port
Add Node Info in Testbed Setup
  Port Number
  IP Address
Use Netty Framework for Server
  Handshaking
  Authenticating Peers
  Establishing Connections
  Preparing the Network for Data Transfer
Monitor Process and Performance

## Slide 12: Communication and Data Transfer Processes
25.03.2024
        Communication and Data transfer Processes
Initial Notification by the LectureStudio Server
  Notification to Tracker Peer
  Start of Data Transfer Process
Role of Super Peers
  Reception and Forwarding of PDF File
  Transition from Receiver to Sender
Confirmation Messages
  From Peers and Super Peers
Calculation of Data Transfer Duration
  Counting Received Confirmations
  Total Duration Calculation
Integrity Checks of PDFs with Hash Value Calculation
Connection and Communication Strategy

## Slide 13: Evaluation Research Questions
Evaluation Research Questions
Testbed
RQ1.1 How Accurately Does the Testbed Measure the Configured Bandwidth, Latency and Packet Loss?
RQ1.2 How Well Does the Testbed Scale with More Nodes and Complex Topologies Affects The Host in Terms of Resource Utilization?
P2P Algorithm
RQ2.1 How Do CPU and Memory Usage Change of the Participants (the LectureStudio Server and Peers) in Tests with and without the P2P Algorithm?
RQ2.2 How Does the P2P Algorithm React to Changing Network Characteristics (Bandwidth, Latency, Packet Loss)?
RQ2.3 Overall, is the P2P Algorithm Efficient for Data Transfer? How Does the Total Duration Obtained with the P2P Algorithm Respond to the Changing Number of Peers and Data Size?
25.03.2024

## Slide 14: Accuracy of the Testbed, RQ1.1 (1)
ACCUracy of the testbed, rq1.2
25.03.2024
Error Rate for Latency with the P2P Algorithm
Error Rate for Latency without the P2P Algorithm
Discrepancy between Desired and Measured Values
More Nodes Decrease Bandwidth Allocation Per Connection
  A Reduction in Bandwidth Corresponds to a Rise in Latency
High CPU and Memory Usage Impacting Network Performance and Latency

## Slide 15: Accuracy of the Testbed, RQ1.1 (2)
ACCUracy of the testbed, rq1.1
25.03.2024
Error Rate for Bandwidth with the P2P Algorithm
Error Rate for Bandwidth without the P2P Algorithm
Accuracy of Measuring Tools
  Iperf Accuracy Results Variation from Actual Performance
  Variables Like Network Conditions, Configuration, System Overhead

## Slide 16: Testbed Scaling and Resource Utilization, RQ1.2
Testbed scaling and resource utilization, rq1.2
25.03.2024
Duration of Deploying and Destroying of Containerlab
CPU and Memory Usage of the Host
Scaling Peers with Containerlab for Simplified Topology Deployment
Deployment Time Increase of 5.37s per Additional Node
Destroying Process Time Low, Approximately 9 Seconds for 75 Nodes
CPU and Memory Usage Rise with More Peers Indicating Increased Host Load
CPU and Memory Utilization Increase Linearly Showing Scalable Performance
Memory Usage Growth Suggests Potential Bottleneck with More Peers

## Slide 17: CPU and Memory Usage Analysis of Nodes, RQ2.1 (1)
Evaluation Setup
Analysis of Resource Consumption (CPU and Memory Usage) of the P2P Algorithm Components (LectureStudio Server and Peers)
High Initial CPU Usage on LectureStudio Server at Data Transfer Start
Peak CPU Usage Reduction of 52% by the P2P Algorithm
Load Distribution Leading to Decreased CPU Usage
25.03.2024
CPU Usage with the P2P Algorithm
CPU Usage without the P2P Algorithm

## Slide 18: CPU and Memory Usage Analysis of Nodes, RQ2.1 (2)
Evaluation Setup
25.03.2024
Memory Usage with the P2P Algorithm
Memory Usage without the P2P Algorithm
Memory Usage Reduction of 41% by theP2P Algorithm
Resource Savings Due to the P2P Algorithm Utilization
Task Distribution to Super Peers Lowers Server's Memory Usage Requirement

## Slide 19: Performance Evaluation of P2P Algorithm, RQ2.2 and RQ2.3 (1)
25.03.2024
CHALLENGES
Test Duration Measurement from First to Last Acknowledgment Message
  Over 1000 Tests Conducted
  Variation in Data Size or Number of Peers
First Configuration for Real Network Data Simulation in Performance Analysis
  Minimal Performance Difference between the P2P Algorithm and Server-Client Models
Second Configuration with Varied Mean Values for Data Simulation
  The P2P Algorithm Efficiency Increase with More Peers and Larger Data Size
Small File Sizes Limited Benefit from P2P Optimization
Larger File Transfers Indicative of the P2P Algorithm Efficiency
Variation in Average Upload and Download Speeds Across Configurations Affects Performance
  Higher Average Speeds in Second Configuration for Enhanced Network Efficiency, Bottleneck Reduction

## Slide 20: Performance Evaluation of P2P Algorithm, RQ2.2 and RQ2.3 (2)
25.03.2024
CHALLENGES
First Configuration with the LectureStudio Server and 20 Peers
  The P2P Algorithm Performance Little Worse to Traditional Approach
Second Configuration with the LectureStudio Server and 20 Peers
  Transferring 2MB Data Size, the P2P Algorithm Performance Nearly Identical to Traditional Approach
  Transferring 128MB Data Size, the P2P Algorithm Performance 27% Faster than Traditional Approach
Time of Whole Data Transfer with the First Configuration
Time of Whole Data Transfer with the Second Configuration

## Slide 21: Performance Evaluation of P2P Algorithm, RQ2.2 and RQ2.3 (3)
25.03.2024
CHALLENGES
Time of Whole Data Transfer with the First Configuration
Time of Whole Data Transfer with the Second Configuration
First Configuration with the LectureStudio Server and 50 Peers
  Transferring 2MB Data Size, the P2P Algorithm Performance Nearly Identical to Traditional Approach
  Transferring 128MB Data Size, the P2P Algorithm Performance 5% Faster than Traditional Approach
Second Configuration with the LectureStudio Server and 50 Peers
  Transferring 2MB Data Size, the P2P Algorithm Performance 12% Faster than Traditional Approach
  Transferring 128MB Data Size, the P2P Algorithm Performance 35% Faster than Traditional Approach

## Slide 22: Challenges
Finding real network dataset
Configuration of the Network Characteristics for Connections
  Bandwidth Limitation
  Latency Addition
  Packet Loss Simulation
Synchronisation Problem of Total Time
Allocation of Bandwidth for the Connections between the LectureStudio Server and Peers
Measurement of the Network Characteristics for Connections
Data Transmission between the LectureStudio Server and Peers
Monitoring by Grafana, Prometheus and cAdvisor
25.03.2024
CHALLENGES

## Slide 23: Conclusion and Future Work
Goal: Develop a Testbed for the P2P Data Distribution Algorithm
  Utilization of Docker and Containerlab for An Efficient, Isolated Testing Environment
Simulation of Real Network Environments and Complex Network Topologies
  High Replication Accuracy of Bandwidth and Latency
  Effective Scalability with Increasing Nodes
High Resource Demand without the P2P Algorithm; Significant Reduction with the P2P Algorithm
  Effective Data Distribution and Reduced Server Load through the P2P Algorithm
Limited P2P Benefits for Small Files and Efficiency Improvements in Different Configurations
Robustness of the P2P Algorithm with Increased Peers and Data Size
Enhancement of Packet Loss Simulation for Accurate Network Behavior
Automation between the Testbed and the P2P Algorithm Optimization
Development of A Graphical Testbed Interface for Easier Configuration and Real-Time Analysis
25.03.2024
CHALLENGES

## Slide 24: Thank you for your attention!
Any questions?
questions
25.03.2024

## Slide 25: References
[1] https://www.data.gov.uk/dataset/dfe843da-06ca-4680-9ba0-fbb27319e402/uk-fixed-line-broadband-performance
[2] https://www.speedtest.net/
[3] https://containerlab.dev/manual/topo-def-file/
References
25.03.2024